New Public Water Systems

To aid you in submitting a complete application to the Bureau of Safe Drinking Water (BSDW), here is a brief summary of the information and data requirements that comprise the public water system permitting process.  Please keep in mind that this summary, while reasonably complete, may not necessarily enumerate every requirement contained in NAC 445A, “Public Water Systems Design, Construction, Operation and Maintenance”.  You are encouraged to review this and other regulations to personally ascertain applicable sections.

The process of securing a permit to operate a non-transient non-community public water system in Nevada is four fold:

- Design and construction of facilities and components of the water system must be in accordance with State requirements, detailed in NAC 445A “Public Water Systems Design, Construction, Operation and Maintenance”.

- Water quality must conform to drinking water standards, per NAC 445A “Public Water Systems Water Quality”.

- The water system owner must demonstrate that he/she has the required technical, managerial and financial capability to operate the water system, as specified by NAC 445A, LCB File No. R073-99.  Among other information, this regulation prescribes that the following plans be submitted:

  - cross-connection control (backflow)

  - emergency

  - operation and maintenance

  - information related to the policies and procedures of the water system, as well as budgetary and financial plans, must also be submitted for review and approval prior to permitting.

- An operator, certified by BSDW, must be in charge of the water system.

Any existing water system components of an un-permitted water system are not “grandfathered” or exempted from design and construction regulations.  A Nevada professional engineer must provide BSDW with plans and specifications of sufficient detail to determine whether or not any “as-built” facilities are adequate.  This also applies to well construction, should the well already be fitted with a pump and discharge piping.

Information related to the policies and procedures of the water system, as well as budgetary and financial plans, must also be submitted for review and approval prior to permitting.

Among additional information required is the following:

Design Report

- Provide a design report that describes the proposed water system, the basis of design, criteria for supply and demand, etc.

- Provide a network hydraulic analysis of the water system, which serves to size water system components and ensures that performance standards are met.

##### Source Water

- Provide evidence of water rights of acceptable amount and character.

- Provide a well log of any existing wells intended for use to verify the presence or absence of a sanitary seal and to depict casing information.  Note that existing facilities are not “grandfathered”.

- Provide well construction details, drawn as part of the plans, including wellhead piping and equipping details (venting, well-to-waste, valves, piping, sampling tap, access tube, air relief, etc.).  Verify that well casing is at least 18 inches above grade or not subject to flooding.

- Maintain well separation criteria from sources of pollution or contamination.  Provide detail suitable for inclusion in the “Source Water Assessment Program”.

# Storage

Provide plans and specifications for any new storage tank that address the requirements of NAC 445A.67065 through 445A.67095 inclusive.  Provide calculations used to size tank overflow.  Provide lockable access hatch and cage, hand rails, correct sized screening on vents, angled flapper or air gap on discharge and overflow lines, silt stop, sampling tap, staff gauge, 30-inch man ways, NSF approved coating, etc.  Specify VOC and total coliform sampling per NAC.  Specify telemetry system and controls to monitor, alarm, and regulate storage.

Specify additional design criteria for any new tank:

- seismic zone

- snow loading

- wind loading and exposure

- soils report

After conceptual approval of any storage facilities by BSDW, please provide this office with professionally engineered calculations for the tank structure and foundation when they become available after bid award.

# Water Treatment

Are provisions for chlorination proposed?  If so, provide design information. An emergency eyewash station would be required, per OSHA.  Propose appropriate treatment for any constituents that don’t meet State Drinking Water Standards.  Submit plans and specifications.

# Pump Station

Provide a design of any pumping facilities/pump house, which complies with NAC 445A.66965 through NAC 445A.6706 inclusive.  Provide details of pumping facilities/pump house in plan and profile, which depict components, dimensions, and placement.  Provide architectural and structural details of pump house per NAC 445A.66985.  Provide an electrical plan.  Provide a slab reinforcing detail.

# Distribution System

Provide required isolation valves.  Provide plan and profile of water lines.  Provide for air releases as required.  Maintain required water line/sewer line separations, including those for laterals. Provide a separation standard detail.  Specify angle fittings to accomplish pipe bends, rather than bending the pipe beyond the manufacturer’s approved bending radius.  Provide standard details of corp stops and curb stops or meter stops on the service lines.  Include backflow prevention, as appropriate.  Be sure to isolate process, fire and irrigation water from potable water.  The distribution system is to be looped, if possible.

# Disinfection and Testing

Specify disinfection of distribution lines per AWWA Standard C-651 and pressure testing per AWWA Standard C-605.

# Water Quality

Data will need to be provided from the source.  Required water quality sampling data are summarized as follows: Regulated Phase I, II, and V Volatile Organics, Regulated Phase II and V Synthetic Organics, Regulated Phase II and V Inorganics, Dioxin, Lead and Copper, Arsenic, Secondary Drinking Water Standards, Total Coliform and Fecal Coliform/E. Coli.  Water quality samples may be composited by a certified laboratory.

#### Technical, Managerial, Financial Capability

Fill out enclosed forms.

#### Water Well Location

Plot on a map all potential sources of pollution or contamination within 150 feet of the well.

Vulnerability Assessment (voluntary)

Identify all potential sources of pollution or contamination to groundwater within a 3,000	foot radius of the well on a 1:24,000 USGS topographic map (7.5-minute map).  Refer to the attached example and list of potential contaminant sources.  Based upon a determination by BSDW of the susceptibility of the well to contamination, BSDW may authorize a reduction in the frequency for water quality monitoring of the source for the presence of certain contaminants.

A copy of “REGULATIONS FOR PUBLIC WATER SYSTEMS” NAC 445A.450 TO 445A.6731 may be downloaded from http://www.leg.state.nv.us/NAC/NAC-445A.html.

Please call Jim Balderson at 775-687-9517 for additional information.

Attachments:  Application for Approval of a Water Project

Potential Contamination Sources

State Certified Methodologies

Plan to Permit a Public Water System

NEVADA DIVISION OF ENVIRONMENTAL PROTECTION

BUREAU OF SAFE DRINKING WATER

901 S. STEWART STREET, SUITE 4001		               2030 E. FLAMINGO RD. STE.230

CARSON CITY, NV 89701				      LAS VEGAS, NV 89119

PHONE:  775-687-9520; FAX:  775-687-5699		PHONE:  702-486-2850 x 221; FAX:  702-486-2863

APPLICATION FOR APPROVAL OF A WATER PROJECT

| PWS Name: | PWS Phone #: |
| --- | --- |
| PWS Number: | PWS Fax #: |
| PWS Address: | PWS Emergency Phone #: |
|  | PWS Email: |

| PWS Contact Name: | PWS Contact Phone #: |
| --- | --- |
| PWS Contact Email: | PWS Contact Fax #: |
| PWS Contact Address: | PWS Contact Emergency Phone(s) #: |

| Submitting Engineer Name: | Engineer Phone #: |
| --- | --- |
| Engineer Email: | Engineer Fax #: |
| Engineer Firm Address: | Engineer Emergency Phone(s) #: |

Date of application submittal:

County in which the water project is located:

Are two copies of wet stamped plans and specifications submitted with this application?	Yes     No

Is the appropriate review fee attached?							Yes     No

(fee schedule located at http://ndep.nv.gov/bsdw/docs/fee04.pdf)

Brief Description and Purpose of the Project:

Estimated Construction Begin Date:

Estimated Construction Completion Date:

Complete the following with assistance from the public water system.

Public Water System Type:	Community	NTNC	TNC

PWS Ownership Type:  		Public     	Private	Homeowner     Federal     GID     Other:

| Population Served: | # of Service Connections: | # of Metered Connections: |
| --- | --- | --- |

Are any of the above parameters changing due to this project?  Yes     No

If yes, describe the changes:

Provide a flow diagram from source through treatment to the distribution system.  Is it attached?     Yes

EXISTING PUBLIC WATER SYSTEMS

Is the proposed project an expansion or modification of an existing water system?		Yes     No

Is the proposed project to re-activate a public water system?				Yes     No

Is this project for a water system that is regulated by the PUC?  				Yes     No

Please refer to the following NAC 445A sections for specific regulatory requirements regarding public water system design and operation.  Verify that all components are addressed and meet the minimum requirements of NAC 445A.

CHECK ALL THAT APPLY TO THIS PROJECT.

Public Water Systems

Water Quality

(NAC 445A.450 to .492)

Surface Water Treatment

(NAC 445A.495 to .540)

Groundwater Treatment

(NAC 445A.54022 to .5405)

PER-Groundwater Treatment

(NAC 445A.54026)

Operation Community or Non-transient Water System

(NAC 445A.591 to .5926)

Permits to Operate Privately Owned Systems

(NAC 445A.595 to .614)

Certification of Operators

(NAC 445A.617 to .652)

Design, Construction, Operation & Maintenance

Emergency Response Plan

(NAC 445A.66665)

O & M Manual

(NAC 445A.6667)

Existing & new systems – Capacity

(NAC 445A.6672 to .66755)

Treatment Facilities

(NAC 445A.6676 to .66815)

Disinfection

(NAC 445A.66825 to .6685)

Water Wells

(NAC 445A.66855 to .6693)

Springs

(NAC 445A.66935 to .6696)

Pumping Facilities

(NAC 445A.66965 to .6706)

Storage Structures

(NAC 445A.67065 to .67095)

Distribution System

(NAC 445A.67105 to .67145)

Separation of Lines

(NAC 445A.6715 to .6718)

Cross-Connection Control Plan

(NAC 445A.67185)

Cross-Connections and Backflow

(NAC 445A.67185 to .67255)

Water Hauling

(NAC 445A.67275 to .6731)

NEW PROJECT INFORMATION ONLY

Include only information related to the new project below.  Do not provide existing water system information unless it is pertinent to the new project.  Leave sections that do not apply to the new project blank (or type “N/A”).

Source Type:

Groundwater well  		Yes     No		Groundwater Spring  		Yes     No

Surface Water Intake		Yes     No		Spring UDI			Yes     No

Purchased Water		Yes     No		System has water rights?	Yes     No

Source(s) master metered?	Yes     No

Source Location:

Meets flood plain requirements?  				Yes     No

Are all sources of potential pollution identified?  		Yes     No

Are there any sources of contamination within 150 feet?		Yes     No

Source Water Quality:

Meets all NAC requirements?  				Yes     No

Requires treatment to meet requirements?	 	Yes     No

Well Characteristics:

| Casing Depth (ft.): | Pump Type: |
| --- | --- |
| Casing Diameter (in): | Max. Production (gpm): |
| Sanitary Seal Depth (ft): | Source Design Capacity (gpm): |
| Emergency Power Provided? Yes No | Average Daily Demand (gpm): |
| Describe Emergency Power: | Emergency Source Capacity (gpm): |

Storage Characteristics:

Storage tank type and material:

Tank capacity (gallons):

Storage tank coating material:

Transmission/Distribution System Characteristics:

Approved pipe material type:

Distribution main size(s):

Linear feet of pipe:

Distribution system pressure range(s):

Number of pressure zones:

Required Fire Flow – fill in below and also provide documentation from the local fire authority or State Fire Marshal For Carson City, Clark and Washoe Counties, required fire flow per the local fire authority: Hydrant (gpm) = Sprinkler System (gpm) = For All Other Counties, required fire flow per the State Fire Marshal: Hydrant (gpm) = Sprinkler System (gpm) =

Can the new main be sampled for coliform bacteria after disinfection every 1200 feet per AWWA Standard C651 requirements? Yes No If no, explain:

Booster Pump Stations:

| Pump Type: | # of pumps: |
| --- | --- |
| Max. Production (gpm): | Source Design Capacity (gpm): |
| Describe Emergency Power: |

Treatment:

| Contaminant(s) that require treatment: |
| --- |
| Treating Groundwater Treating Surface Water |
| Unit Processes & Associated Chemical Addition: |
| Flow Rate (gpd): | Flow Rate (gpm): |
| Design Capacity (gpd): |  |
| A schematic of the treatment system is required. Is it attached? Yes |
| Describe the Process Flow from source to treatment to distribution: |

Chlorination for system residual only:

Type of disinfectant used:

NSF approved chemicals used? Yes No

Does the system use continuous automatic disinfection? Yes No

Where are the disinfection systems located?

Where are the chemicals stored?

SCADA/Telemetry:

Does the public water system utilize SCADA/Telemetry? Yes No

Which facilities are part of the SCADA/Telemetry system?

Inter-Tie:

| Name of other system: | Anticipated date of inter-tie: |
| --- | --- |
| Reason for inter-tie (check all that apply): Normal Operations Intermittent Seasonal Emergency Other, explain: |
| Flow is: one-way; Discuss direction and % of flow: two-way; Discuss direction and % of flow: |
| Is the inter-tie part of a regional water system? Yes No If Yes, explain: |

Consolidation:

| Name of other system: | Anticipated date of consolidation: |
| --- | --- |
| Supplier of water: |

Program to Assess Vulnerability, NAC 445A.6668, (optional):

Was a completed vulnerability assessment submitted for all sources? Yes No

Does the document contain sufficient information to issue monitoring waivers? Yes No

Are all of the potential contaminant sources within 3000 feet of the well/spring located on a 1:24,000 U.S.G.S. Quad Map (7.5-minute map)? Yes No

Water Hauling:

A water hauling plan is required. Is it attached? Yes

Is this for an existing water hauler? Yes No

If yes, please provide water hauler permit number(s):

Public water system hauling from:

Public water system hauling to:

NEW PUBLIC WATER SYSTEMS

(An overview of the requirements to becoming a public water system can be found at http://ndep.nv.gov/bsdw/nws.htm)

Is the proposed project a new public water system?					Yes     No

If Yes, check type:  Community    Non-Transient Non-Community    Transient Non-Community

Is this project to permit a privately owned community (residential) system?  		Yes     No

New Community Publicly Owned Public Water System must also submit the following:

Plan to Permit a Public Water System**

Plan for Restoration of Services in Emergency (draft version acceptable)

Cross-Connection Control Plan (draft version acceptable)

Manual of Operations and Maintenance (draft version acceptable)

New Community Privately Owned Public Water System must also submit the following:

Plan to Permit a Public Water System**

Plan to Permit a Privately Owned Public Water System**

Plan for Restoration of Services in Emergency (draft version acceptable)

Cross-Connection Control Plan (draft version acceptable)

Manual of Operations and Maintenance (draft version acceptable)

New Non-Transient Non-Community Public Water System must also submit the following:

Plan to Permit a Public Water System**

Plan for Restoration of Services in Emergency (draft version acceptable)

Cross-Connection Control Plan (draft version acceptable)

Manual of Operations and Maintenance (draft version acceptable)

New Transient Non-Community Public Water System must also submit the following:

Plan for Restoration of Services in Emergency (draft version acceptable)

Cross-Connection Control Plan (draft version acceptable)

Manual of Operations and Maintenance (draft version acceptable)

** “Plan to Permit” forms are located at http://ndep.nv.gov/bsdw/epr-docs.htm.

POTENTIAL CONTAMINATION SOURCES

(* Denotes GPS location required)

|  | Agricultural | Contaminant Category | Risk Ranking Category |  | Medical/Educational | Contaminant Category | Risk Ranking Category |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Animal burial areas | C, D | High | 28 | Educational institutions (labs, lawns, & | B, C | Moderate |
| 2 * | Animal feedlots | B, C, D | High, in Zone A; otherwise moderate |  | chemical storage areas) |  |  |
| 3 | Chemical application (e.g. pesticides, fungicides, & fertilizers) | C, B | High | 29 | Medical institutions (medical dental, vet offices) | D, E | Low |
| 4 * | Chemical mixing & storage areas | A, B, C | High | 30 * | Research laboratories | A, B, C, D, E | High |
|  | (including rural airports) |  |  |  |  |  |  |
| 5 | Irrigated fields Irrigation ditches | B C | Moderate High |  | Storage |  |  |
| 6 | Manure spreading & pits | A, C | Moderate | 31 * | Aboveground storage tanks | A, B | High |
| 7 * | Unsealed irrigation wells | A, B, C, D | High | 32 * | Underground storage tanks | A | High |
|  |  |  |  | 33 | Public storage | A | Low |
|  | Industrial |  |  | 34 * | Radioactive materials storage | E | High |
| 8 * | Chemical manufacturers, | A, B, C | High |  |  |  |  |
|  | Warehousing/distribution activities |  |  |  | Municipal waste |  |  |
| 9 * | Electroplaters & fabricators | C | High | 35 * | Dumps and landfills (historical/active) | A, B, C, D, E | High |
| 10 * | Electrical products & manufacturing | C | High | 36 | Municipal incinerators | B, C, D | Moderate |
| 11 * | Machine & metalworking shops | A | High | 37 * | Recycling & reduction facilities | C | High |
| 12 * | Manufacturing sites | A, B, C | High | 38 * | Scrap & junkyards | A, C | High |
| 13 * | Petroleum products production, | A | High | 39 * | Septage Lagoons, wastewater | A, B, C, D | High |
|  | Storage & distribution centers |  |  |  | treatment plants, injection wells |  |  |
|  |  |  |  | 40 * | Sewer Transfer Stations | A, B, C, D | High |
|  | Commercial |  |  |  | Miscellaneous |  |  |
| 14 * | Dry cleaning establishments | A | High | 41 * | Airports | A | High |
| 15 * | Furniture & wood stripper & | A | High | 42 * | Asphalt plants | A | High |
|  | Refinishers |  |  | 43 | Boat yards | A | High |
| 16 * | Jewelry & Metal plating | C | High | 44 | Cemeteries | D | Moderate |
| 17 | Laundromats | C | Low | 45 | Construction areas | A | Moderate |
| 18 * | Paint shops | A | High | 46 * | Dry wells | A, D | High |
| 19 * | Photography establishments & | C | High | 47 * | Fuel storage systems | A | High |
|  | Printers |  |  | 48 | Golf courses, parks & nurseries | B, C | High |
|  |  |  |  |  | (chemical application) |  |  |
|  | Automotive |  |  | 49 | Mining (surface & underground) | A, C | High |
| 20 * | Auto repair shops | A, C | High | 50 | Pipelines (oil, gas, coal slurry) | A | High |
| 21 | Car washes | A, C, D | Moderate | 51 * | Railroad tracks, yards & maintenance | A, B, C, D | High |
| 22 * | Gas stations | A, C | High | 52 | Surface water impoundments, | D | High |
| 23 | Road deicing operations: storage & | C | Moderate |  | streams/ditches |  |  |
|  | Application areas (e.g. road salt) |  |  | 53 * | Stormwater drains & retention basins | A, B, C, D, E | High |
| 24 * | Road maintenance depots | A, C | High | 54 * | Unplugged abandoned well | A, B, C, D | High |
|  |  |  |  | 55 * | Well: operating | A, B, C, D | High(Low |
|  | Residential |  |  | 56 | Other – please specify |  |  |
| 25 | Household hazardous products | A, B, C | Moderate |  |  |  |  |
| 26 | Private wells | A, B, C, D | Moderate |  |  |  |  |
| 27 | Septic systems, cesspools | B, C, D | High, if Zone A; otherwise moderate |  |  |  |  |

Contaminant Categories:		A = V.O.C.

B = S.O.C.

C = I.O.C.

D = MICROBIOLOGICAL

E = RADIONUCLIDES

July 26, 2000

| REGULATED SYNTHETIC ORGANIC CHEMICALS (SOCs) 40 CFR 141.24 (e) & 141.61 (c), Federal Register Vol. 76, No. 122 and Vol. 77, No. 125 |
| --- |
| PHASE II |
| Contaminant | Approved Methods | MCL (mg/L) parts per million | MCL (µg/L) parts per billion |
| (1) | 2051 | ALACHLOR (LASSO) | 505, 507, 508.1, 525.2, 525.3, 551.1 |  | 0.002 |  | 2 |
| (2) | 2050 | ATRAZINE | 505, 507, 508.1, 523, 525.2, 525.3, 536, 551.1, Syngenta 5 AG-625 |  | 0.003 |  | 3 |
| (3) | 2046 | CARBOFURAN | 531.1, 531.2, 6610, 6610B |  | 0.04 |  | 40 |
| (4) | 2959 | CHLORDANE | 505, 508, 508.1, 525.2, 525.3 |  | 0.002 |  | 2 |
| (5) | 2931 | DIBROMOCHLOROPROPANE (DBCP, 1,2-Dibromo-3-Chloropropane) | 504.1, 524.3, 551.1 |  | 0.0002 |  | 0.2 |
| (6) | 2946 | ETHYLENE DIBROMIDE (EDB or Dibromoethane) | 504.1, 524.3, 551.1 |  | 0.00005 |  | 0.05 |
| (7) | 2065 | HEPTACHLOR | 505, 508, 508.1, 525.2, 525.3, 551.1 |  | 0.0004 |  | 0.4 |
| (8) | 2067 | HEPTACHLOR EPOXIDE | 505, 508, 508.1, 525.2, 525.3, 551.1 |  | 0.0002 |  | 0.2 |
| (9) | 2010 | LINDANE (BHC-GAMMA) | 505, 508, 508.1, 525.2, 525.3, 551.1 |  | 0.0002 |  | 0.2 |
| (10) | 2015 | METHOXYCHLOR | 505, 508, 508.1, 525.2, 525.3, 551.1 |  | 0.04 |  | 40 |
| (11) | 2383 | POLYCHLORINATED BIPHENYLS (as AROCLORS) – regulated as decachlorobiphenyl | 505, 508, 508.1, 525.2, 525.3 |  | 0.0005 |  | 0.5 |
| (11a) | 2383 | POLYCHLORINATED BIPHENYLS (as decachlorobiphenyl) 2388, 2390, 2392, 2394, 2396, 2398, 2400 | 508A is used to quantitate individual Aroclors detected using 505 or 508. |  | 0.0005 |  | 0.5 |
| (12) | 2326 | PENTACHLOROPHENOL | 515.1, 515.2, 515.3, 515.4, 525.2, 525.3, 555, 6640B |  | 0.001 |  | 1 |
| (13) | 2020 | TOXAPHENE | 505, 508, 508.1, 525.2, 525.3, |  | 0.003 |  | 3 |
| (14) | 2105 | 2,4-D | 515.1, 515.2, 515.3, 515.4, 555, D5317-93/98, 6640B |  | 0.07 |  | 70 |
| (15) | 2110 | 2,4,5-TP (Silvex) | 515.2, 555, 515.1, 515.3, 515.4, D5317-93/98, 6640B |  | 0.05 |  | 50 |
| PHASE V |
| (1) | 2306 | BENZO(a)PYRENE | 525.2, 525.3, 550, 50.1 |  | 0.0002 |  | 0.2 |
| (2) | 2031 | DALAPON | 552.1, 552.2, 552.3, 515.1, 515.3, 515.4, 557, 6640B |  | 0.2 |  | 200 |
| (3) | 2035 | DI(2-ETHYLHEXYL)ADIPATE | 506, 525.2, 525.3 |  | 0.4 |  | 400 |
| (4) | 2039 | DI(2-ETHYLHEXYL)PHTHALATE | 506, 525.2, 525.3 |  | 0.006 |  | 6 |
| (5) | 2041 | DINOSEB | 515.2, 555, 515.1, 515.3, 515.4, 6640B |  | 0.007 |  | 7 |
| (6) | 2032 | DIQUAT | 549.2 |  | 0.02 |  | 20 |
| (7) | 2033 | ENDOTHALL | 548.1 |  | 0.1 |  | 100 |
| (8) | 2005 | ENDRIN | 505, 508, 508.1, 525.2, 525.3, 551.1 |  | 0.002 |  | 2 |
| (9) | 2034 | GLYPHOSATE | 547, 6651, 6651B |  | 0.7 |  | 700 |
| (10) | 2274 | HEXACHLOROBENZENE | 505, 508, 508.1, 525.2, 525.3, 551.1 |  | 0.001 |  | 1 |
| (11) | 2042 | HEXACHLOROCYCLOPENTA-DIENE | 505, 508, 508.1, 525.2, 525.3, 551.1 |  | 0.05 |  | 50 |
| (12) | 2036 | OXYMAL (VYDATE) | 531.1, 531.2, 6610, 6610B |  | 0.2 |  | 200 |
| (13) | 2040 | PICLORAM (PICHLORAM) | 515.2, 515.1, 515.3, 515.4, 555, D5317-93/98, 6640B |  | 0.5 |  | 500 |
| (14) | 2037 | SIMAZINE | 505, 507, 508.1, 523, 525.2, 525.3, 536, 551.1 |  | 0.004 |  | 4 |
| (15) | 2063 | 2,3,7,8-TCDD (DIOXIN) | 1613 |  | 3 x 10(-8 |  |  |
| REGULATED VOLATILE ORGANIC CHEMICALS (VOCs) 40 CFR 141.24 (e) & 141.61 (c), Federal Register Vol. 74, No. 147, Vol. 76, No. 122 and Vol. 77, No. 125 |
| PHASE I AND II |
| Contaminant | Approved Methods | MCL (mg/L) parts per million | MCL (µg/L) parts per billion |
| (1) | 2990 | BENZENE | 502.2, 524.2, 524.3 |  | 0.005 |  | 5 |
| (2) | 2982 | CARBON TETRACHLORIDE | 502.2, 524.2, 524.3, 551.1 |  | 0.005 |  | 5 |
| (3) | 2989 | CHLOROBENZENE (MONOCHLOROBENZENE) | 502.2, 524.2, 524.3 |  | 0.1 |  | 100 |
| (4) | 2968 | 1,2-DICHLOROBENZENE (ortho-) | 502.2, 524.2, 524.3 |  | 0.6 |  | 600 |
| (5) | 2969 | 1,4-DICHLOROBENZENE (para-) | 502.2, 524.2, 524.3 |  | 0.075 |  | 75 |
| (6) | 2980 | 1,2-DICHLOROETHANE | 502.2, 524.2, 524.3 |  | 0.005 |  | 5 |
| (7) | 2978 | 1,1-DICHLOROETHYLENE (DICHLOROETHENE) | 502.2, 524.2, 524.3 |  | 0.007 |  | 7 |
| (8) | 2380 | CIS-1,2-DICHLOROETHYLENE (CIS-1,2-DICHLOROETHENE) | 502.2, 524.2, 524.3 |  | 0.07 |  | 70 |
| (9) | 2979 | TRANS-1,2-DICHLOROETHYLENE (TRANS-1,2-DICHLOROETHENE) | 502.2, 524.2, 524.3 |  | 0.1 |  | 100 |
| (10) | 2983 | 1,2-DICHLOROPROPANE | 502.2, 524.2, 524.3 |  | 0.005 |  | 5 |
| (11) | 2992 | ETHYLBENZENE | 502.2, 524.2, 524.3 |  | 0.7 |  | 700 |
| (12) | 2996 | STYRENE | 502.2, 524.2, 524.3 |  | 0.1 |  | 100 |
| (13) | 2987 | TETRACHLOROETHYLENE (PCE) (TETRACHLOROETHENE) | 502.2, 524.2, 524.3, 551.1 |  | 0.005 |  | 5 |
| (14) | 2991 | TOLUENE | 502.2, 524.2, 524.3 |  | 1 |  | 1,000 |
| (15) | 2981 | 1,1,1-TRICHLOROETHANE | 502.2, 524.2, 524.3, 551.1 |  | 0.2 |  | 200 |
| (16) | 2984 | TRICHLOROETHYLENE (TCE) (TRICHLOROETHENE) | 502.2, 524.2, 524.3, 551.1 |  | 0.005 |  | 5 |
| (17) | 2976 | VINYL CHLORIDE | 502.2, 524.2, 524.3 |  | 0.002 |  | 2 |
| (18) | 2955 | XYLENES (TOTAL OF M,P & O) | 502.2, 524.2, 524.3 |  | 10 |  | 10,000 |
| PHASE V |
| (1) | 2964 | DICHLOROMETHANE (METHYLENE CHLORIDE) | 502.2, 524.2, 524.3 |  | 0.005 |  | 5 |
| (2) | 2378 | 1,2,4-TRICHLOROBENZENE | 502.2, 524.2, 524.3 |  | 0.07 |  | 70 |
| (3) | 2985 | 1,1,2-TRICHLOROETHANE | 502.2, 524.2, 524.3, 551.1 |  | 0.005 |  | 5 |

| REGULATED INORGANIC CHEMICALS (IOCs) 40 CFR 141.23 (k) & 141.62 (b), Federal Register Vol. 76, No. 122 and Vol. 77, No. 125 |
| --- |
| PHASE II |
| Contaminant | Approved Methods | MCL (mg/L) parts per million | MCL (µg/L) parts per billion |
| (1) | 1025 | FLUORIDE | 300.0, 300.1, 4110B, 129-71W, 380-75WE, D4327, D1179-B, 4500-F- B/C/D/E, Hach SPADNS 2 m. 10225 | 4 |  | 4000 |
| (2) | 1010 | BARIUM | 200.7, 200.8, 3111D, 3113B, 3120B | 2 |  | 2000 |
| (3) | 1015 | CADMIUM | 200.7, 200.8, 200.9, 3113B | 0.005 |  | 5 |
| (4) | 1020 | CHROMIUM | 200.7, 200.8, 200.9, 3113B, 3120B, D6919 | 0.1 |  | 100 |
| (5) | 1030 | LEAD | 200.8, 200.9, 3113B, D3559-D, Hach/Palintest 1001 | 0.015 (Action Level) |  |  |
| (6) | 1035 | MERCURY | 245.1, 245.2, 200.8, 3112B, D3223 | 0.002 |  | 2 |
| (7) | 1045 | SELENIUM | 200.8, 200.9, 3113B, 3114B, D3859-A, D3859-B | 0.05 |  | 50 |
| (8) | 1040 | NITRATE | 300.0, 300.1, 353.2, 4110B, 601, B-1011, 4500-NO3- B/D/E/F, D3867A, D3867-B, D4327, D6508, Systea Easy, Hach TNTplus 835/836 m. 10206 | 10 (as N) |  | 10000 |
| (9) | 1041 | NITRITE | 300.0, 300.1, 353.2, D4327, D3867-A, D3867-B, 4110B, 4500-NO3 - E/F, B-1011, 4500-NO2 – B, D6508 | 1 (as N) |  | 1000 |
| (10) | 1038 | TOTAL NITRATE + NITRITE | See above | 10 (as N) |  | 10000 |
| (11) | 1094 | ASBESTOS | 100.1, 100.2 | 7 Million Fibers/L longer than 10um |  |  |
| PHASE V |
| (1) | 1074 | ANTIMONY | 200.8, 200.9, 3113B, D3697 |  | 0.006 |  | 6 |
| (2) | 1075 | BERYLLIUM | 200.7, 200.8, 200.9 3113B, 3120B, D3645-B |  | 0.004 |  | 4 |
| (3) | 1024 | CYANIDE | 335.4, D2036-A, D2036-B, D6888, 4500-CN- C/E/G/F, OIA-1677 DW, I-3300-85, Kelada-01, QuikChem 10-204-00-1-X |  | 0.2 |  | 200 |
| (4) | 1036 | NICKEL | 200.7, 200.8, 200.9, 3111B, 3113B, 3120B |  | N/A |  | N/A |
| (5) | 1085 | THALLIUM | 200.8, 200.9 |  | 0.002 |  | 2 |
| (40 CFR 141.11 (a)) |
| Contaminant | Approved Methods | MCL (mg/L) parts per million | MCL (µg/L) parts per billion |
| (6) | 1005 | ARSENIC (January 23, 2006) | 200.8, 200.9, D2972-B, D2972-C, 3113B, 3114B |  | 0.010 |  | 10 |

| SECONDARY DRINKING WATER STANDARDS NAC 445A.455 & 40 CFR 143.4, , Federal Register Vol. 76, No. 122 and Vol. 77, No. 125 |
| --- |
|  |  | Contaminant | Approved Methods | MCL(mg/L) parts per million |
| (1) | 1002 | ALUMINUM | 200.7, 200.8, 200.9, 3111D, 3113B, 3120B |  | 0.2 |
| (2) | 1017 | CHLORIDE | 300.0, 300.1, 4110B, 4500-Cl- B/D, D4327, D512-B, D6508 |  | 400 |
| (3) | 1905 | COLOR | 2120B |  | 15.0 (color units) |
| (4) | 1022 | COPPER | 200.7, 200.8, 200.9, 3111B, 3113B, 3120B, D1688-A, D1688-C |  | 1 |
| (5) | 1025 | FLUORIDE | 300.0, 300.1, 4110B, 129-71W, 380-75WE, D4327, D1179B, 4500-F- B/C/D/E, Hach SPADNS 2 m. 10225 |  | 2 |
| (6) | 1089 | FOAMING AGENTS (MBAS) (METHYLENE BLUE ACTIVE SUBSTANCES) | 5540C |  | 0.5 |
| (7) | 1028 | IRON | 200.7, 200.9, 3111B, 3113B, 3120B |  | 0.6 |
| (8) | 1031 | MAGNESIUM | 200.7, 3111B, 3120B, D511-A, D511-B, 3500-Mg B/E, D6919 |  | 150 |
| (9) | 1032 | MANGANESE | 200.7, 200.8, 200.9, 3111B, 3113B, 3120B |  | 0.1 |
| (10) | 1920 | ODOR | 2150B |  | 3.0 (TON) |
| (11) | 1925 | pH | 150.1, 150.2, D1293, 4500-H+ B |  | 6.5 – 8.5 (pH units) |
| (12) | 1050 | SILVER | 200.7, 200.8, 200.9, 3111B, 3113B, 3120B, I-3720-85 |  | 0.10 |
| (13) | 1055 | SULFATE | 300.0, 300.1, 375.2, D4327, 4110B, D516, 4500-SO42- C/D/E/F, D6508 |  | 500 |
| (14) | 1930 | TOTAL DISSOLVED SOLIDS (TDS) | 2540C |  | 1,000 |
| (15) | 1095 | ZINC | 200.7, 200.8, 3111B, 3120B |  | 5 |

| TOTAL COLIFORM BACTERIA 40 CFR 141.21 |
| --- |
| Organism | Methodology | Approved Methods |
| Total Coliforms (3100) E. coli (3014) | Total Coliform Fermentation Technique………………………….. Total Coliform Membrane Filter Technique……………………… Presence-Absence (P-A) Coliform Test………………………….. ONPG-MUG Test…………………………………………………… Colisure Test E-Colite® Test m-ColiBlue24® Test Readycult® Coliforms 100 Presence/Absence Test Membrane Filter Technique using Chromocult® Coliform Agar Colitag® Test Chromocult Colilert/Colilert-18……….………………………………………….. | 9221A,B 9222A, B, C 9221D 9223 9223B |

NDEP/BSDW

PLAN TO PERMIT A PUBLIC WATER SYSTEM

OPERATION OF A COMMUNITY OR NONTRANSIENT NONCOMMUNITY WATER SYSTEM UNDER NEVADA ADMINISTRATIVE CODE, CHAPTER 445A.591 THROUGH 445A.5926;

OPERATION PLAN SUBMITTAL

NAC 445A.5921, Submission of Plan;

NAC 445A.5922, Contents of Plan

1.  A description of the community or non-transient non-community water system that includes:

a) Legal description of the proposed area of service including a layout map and township, range and section location;

b) State the purpose of the system and a plan to resolve any operational problems concerning the operation of the system;

c) Describe the program to be submitted for the control of cross-connections as required in NAC 445A.67185;

d) Describe a plan for restoration of services in an emergency as required in NAC 445A.66665;

e) Describe the operation and maintenance plan (to be submitted) that the water system will use in accordance with NAC 445A.6667;

f) Describe the type of water treatment used (if applicable);

g) Describe any unique characteristics of the service area or water system;

2.  An analysis of the managerial capability of the system, including:

a) The name, address and phone number of each owner, manager or operator of the system;

b) The name, address and phone of a person to notify in the case of an emergency;

c) The type of operator certificates held by each operator;

d) The organization, by-laws and policies of the system;

e) The manner in which the system will bill customers and/or correspond with customers;

f) An evaluation of each position employed to manage, operate, or maintain the system, including: job responsibilities, monitoring of state and federal regulations and determining if they apply to management, operation or maintenance of the system; determination of the cost to comply with regulations;

3.  Information concerning planning for the system;

a) Estimated population served by the system;

b) Number of service connections served by the system;

c) Estimated amount of water required for the system:

d) A description of the customers served by the system;

e) An estimate of the proposed use of the property for 20 years in 5 year increments;

4.  An analysis of the technical capability of the system;

a) The standards for the design, construction, operation and maintenance of the system;

b) Analysis of water quality for samples of water from sources supplying the system;

c) A description of the inventory of system components;

5. An analysis of the water resources of the system;

a) A plan for water conservation or water meter effectiveness;

b) The estimated amount of water required for the five year period after startup;

c) Demonstration of the ownership of water rights/appropriation from the State Engineer sufficient to serve the five year period after startup;

d) An analysis of the effect(s) of user discontinuation of service (if any);

e) A plan for responding to any water shortages during the five years after startup;

6.  A description/analysis of other sources of water available to the system, including;

a) A description of each source;

b) Identification of the nearest community or nontransient noncommunity water system to the system;

c) A plan to obtain support for the operation and maintenance of the system from any other system;

d) Any connection that is available to the system from any other system;

e) Reasons for specifying the use of any other source of water for the system;

7.  A program of capital improvements for the system including a schedule for implementation;

a) Identification of any project(s) necessary for the system to begin or maintain the operation of the systems and reasons for the project(s);

b) A schedule that ranks the projects(s) in order of priority;

c) A list of costs incurred by the system for each of the project(s);

d) Each source of money or financing required for each of the project(s);

8.  Demonstration of the financial capability of the system, including;

a) An operating budget for five years after startup of operation that includes the ability of the system to spend money for emergency improvements, capital improvements and normal operation and maintenance of the system;

b) An evaluation of the rate structure and connection fees of the system;

c) An evaluation of the total cost of providing service to the customers of the system;

d) An evaluation of the manner in which the total cost set forth in paragraph c) will be recovered by the system;

e) An evaluation of the stability of the cash flow of the system;

9.  Information concerning any legal matters relating to the system, including;

a) A plan to operate the system if the system is declared bankrupt or is placed into receivership;

b) The ownership of any real property of the system and any buildings located on that property;

c) Any right-of-way, easement or restrictive covenant obtained by the system or which applies to the system;

d) Any contract to which the system is a party or which applies to the system;

10.  A statement that specifies any federal, state or local governmental entity that may adopt regulations concerning the operation of the system or enforce any law or regulation that applies to the system;

11.  Any other pertinent information that the Division may request will be provided.